## Slide 1: Inter Integrated Circuit Bus
The I2C protocol was developed by Philips and is a registered trademark
It is sometimes referred to as a “2 wire interface”
It is typically used to connect low speed peripherals to embedded systems, motherboards etc.

## Slide 2: I2C Connections
I2C only uses two lines
  SDA – Serial Data
  SCL – Serial Clock
Bus capacitance limits the speed of data transfer
This limits the speed of I2C devices to below 400kHz

## Slide 3: Multiple I2C Connections
This protocol allows many slaves to be connected to one master chip
Each device has a 7-bit address
The address is often set by tying pins on the actual device HIGH or LOW
The other address values are built into the device, based on what type of device it is

## Slide 4: Data Transfer
As with SPI, the I2C master supplies the clock on the SCL line
The SDA line can only change when the SCL line is low
When the SCL line is LOW the next bit of data is clocked onto the SDA line
This is done for each bit in turn starting with the MSB

## Slide 5: Start and Stop bits
To signal the start of data transmission the SDA line changes from HIGH to LOW while the SCL line is HIGH
This is known as the start condition
To indicate the end of data transmission the SDA line brought from LOW to HIGH while the SCL line is HIGH
This is known as the stop condition
Apart from the Start and Stop condition, the SDA line must never change state while SCL is HIGH

## Slide 6: Data Acknowledgement
I2C is more complex than SPI
The master device must be able to check whether a device is present and responding
Whenever a byte of data has been transmitted , the receiving device pulls the SDA line LOW for one bit period
This is known as the acknowledge bit
The host can now check if the slave received its data correctly

## Slide 7: Timing Diagrams

## Slide 8: I2C Physical Connections
All I2C devices have either open collector or open drain outputs on their SDA lines
This line is pulled up by an external resistor
This means that devices can not damage each other by asserting different logic levels

## Slide 9: I2C Devices
Examples of I2C devices are:
  24Cxx EEPROM chips
The 24 indicates that is an I2C device and the xx represents the capacity

## Slide 10: GT16’s I2C Module
The GT16 has a dedicated I2C module
This unit sends and receives data
It can be the master or slave
Maximum speed is 100kps
Register controlled

## Slide 11: GT16’s I2C Module

## Slide 12: GT16’s I2C Module
I2C