## Slide 1: On-Line Measurement of Power Quality Parameters Using Signal Processing Techniques

## Slide 2: CONTENTS
  Introduction
  Types of signal processing techniques are use
  MEASUREMENT SYSTEM ARCHITECTURE AND SIMULATION
  FREQUENCY MEASUREMENT.
  HARMONICS MEASUREMENT
  MODELLING OF THE KALMAN FILTER
  FLICKER MEASUREMENT
  WAVELET BASED SIGNAL DECOMPOSITION TECHNIQUE
  HARDWARE PLATFORM
  APPLICATIONS
  CONCLUSIONS

## Slide 3: INTRODUCTION
  This presentation provides an overview of the time varying power quality issues in power systems.
  A new signal processing techniques for real time measurement of various power quality parameters.
  The definition of Power Quality cannot be limited to the characteristics of the supply power. The definition must also include the requirements of the load.
  Signal processing techniques are applied for real time measurement of power quality parameters such as frequency, harmonics, flicker and disturbances.

## Slide 4: Types of signal processing techniques
  (1) Digital filtering technique
  2) Kalman filter technique
  (3) Fast Fourier Transform and statistical method
  (4) Multi-resolution signal decomposition techniques
based on wavelet transform
Four new

## Slide 5: FREQUENCY MEASUREMENT
In many power system protection and control schemes it is necessary to accurately measure and track the fundamental power frequency under sinusoidal and non-sinusoidal conditions
  There are various methods
  zero crossing methods
  FFT leakage
  Stationary phase changes
  Least squares fitting.

## Slide 6: Freq measurement for three phases

## Slide 7: SIMULATION RESULTS
  The method has been tested under various conditions using the simulation software MATLAB.
  Simulation is run for 24 hour period with new inputs every 2 minutes.
  Output can be analyzed for each component individually or collectively by looking at the THD (bottom).
  CASE-I
Error with various harmonic content

## Slide 8: CASE -II
  The method is also tested
for signals with multiple
zero crossing.
  Simulation results
concludes that the
maximum error of this
model is less that 0.005% under non-sinusoidal and multiple zero crossing conditions.
Signal with multiple zero crossing.
Error with multiple zero crossing

## Slide 9: HARMONICS MEASUREMENT
  Due to increased utilization of power electronics devices voltage and current waveforms of a distribution or a transmission system are not pure sinusoids but consist of a combination of the fundamental frequency, harmonics and high frequency transients
  The DFT and FFT transform is a useful analytical tool that has been applied to power system for phasor measurement and harmonic analysis.
  Kalman filtering is a power tool for on line tracking of
amplitudes and phase of power system harmonics

## Slide 10: MODELLING OF THE KALMAN FILTER

## Slide 11: Conti…..
Voltage signal with voltage dip and kalman filter and actual output signal.
Estimated magnitudes of Harmonic components

## Slide 12: FLICKER MEASUREMENT
  Flicker is basically caused by fluctuations of the electrical power network that may occur at any time under the influence of the variations of any of the three components of the network
  Voltage fluctuations up to 30Hz may produce annoyance even if considering small relative amplitudes such as 0.25% at the critical modulation frequency of 8.8Hz
  the use of FFT and new statistical block for real time measurement of flicker in power system.

## Slide 13: SIMULATION RESULTS
  The simulation is carried out in MATLAB for flicker measurement.
  The voltage signal consist of a fundamental component and interharmonic frequency of 8.8Hz.
FFT windows at various record lengths

## Slide 14: WAVELET BASED SIGNAL DECOMPOSITION TECHNIQUE
  Wavelets can determine the presence of transients and harmonic distortions of very small values: up to less than 0.5%.
  With values around 0.1% the detail coefficients can hardly detect the transient and harmonics.
  The color map seems more helpful in identifying both transients and harmonics as the magnitude both transients and harmonics values go bellow 0.5%.

## Slide 15
  This fig shows four level MRA of a distorted signal with sag disturbance.
Four level decomposition of the signal
  The detection and localization of the types of power quality disturbances are generally influenced by the choice of analyzing wavelets.
  d1, d2, d3 and d4 represent the detailed version of the
coefficients and a4 represent the approximated version of the coefficients.

## Slide 16
  Case-a: Voltage Sag
  Case-b: Voltage Swell
Voltage signal with sag and detail coeff d1
Voltage signal with swell and detail coeff d1

## Slide 17: Case-c: Transients
  Using the MRA technique the software was developed
to detect the occurrence and duration of the disturbance
event.
  The energy of the distorted signal and the energy of a non-distorted signal are calculated.
  Depending on the difference in the energy distribution the sag, swell and transients events are
classified

## Slide 22: HARDWARE PLATFORM
  The multiprocessor platform using digital signal processor (DSP) (TMS320F2806). The DSP has internal 12-bit ADC with maximum sampling frequency of 12.5MSPS.

## Slide 23: APPLICATIONS
  A. Feeder Protection and Load Shedding
  B. Harmonic Filter design
  C. Wind Turbines.
  D. Power Quality Disturbance Analysis

## Slide 24: CONCLUSIONS
  In this paper we have proposed high performance signal processing techniques and the proposed digital instrument based on multiple DSP that help to speed up measurement and algorithm execution
  Power Quality has a dynamic, time-varying nature which with the increased complexity and sensitivity of equipment needs to be properly understood and addressed. Traditional methods are not sufficient.
  Advanced techniques and technologies, including real real-time modeling / simulation, power electronics solutions, signal processing and controls applications are available to assist in these tasks.

## Slide 25: THANKS