## Slide 1: DESIGN OF ENERGY SYSTEM

## Slide 2
FLUID DYNAMICS THE BERNOULLI EQUATION
The laws of Statics that we have learned cannot solve Dynamic Problems. There is no way to solve for the flow rate, or Q. Therefore, we need a new dynamic approach to Fluid Mechanics.

## Slide 3
The Bernoulli Equation
By assuming that fluid motion is governed only by pressure and gravity forces, applying Newton’s second law, F = ma, leads us to the Bernoulli Equation.
P/ + V2/2g + z = constant along a streamline (P=pressure  =specific weight V=velocity g=gravity z=elevation)
A streamline is the path of one particle of water. Therefore, at any two points along a streamline, the Bernoulli equation can be applied and, using a set of engineering assumptions, unknown flows and pressures can easily be solved for.

## Slide 4: Bernoulli Equation Applications
Stagnation tube
Pitot tube
Free Jets
Orifice
Venturi
Sluice gate
Sharp-crested weir
Applicable to contracting streamlines (accelerating flow).
Teams

## Slide 5
The Bernoulli Equation (unit of L)
At any two points on a streamline:
P1/ + V12/2g + z1 = P2/ + V22/2g + z2
1
2

## Slide 6
Water is flowing with a velocity of 15 m/s and under a pressure of 300 kPa .If the height above datum is 30 m .calculate Total Energy per unit weight of water
Ans 72 Nm/N

## Slide 7
A Simple Bernoulli Example
 V2
Z
 = air
Determine the difference in pressure between points 1 and 2
Assume a coordinate system fixed to the bike (from this system, the bicycle is stationary, and the world moves past it). Therefore, the air is moving at the speed of the bicycle. Thus, V2 = Velocity of the Biker
Hint: Point 1 is called a stagnation point, because the air particle along that streamline, when it hits the biker’s face, has a zero velocity (see next slide)

## Slide 8
Stagnation Points
On any body in a flowing fluid, there is a stagnation point. Some fluid flows over and some under the body. The dividing line (the stagnation streamline) terminates at the stagnation point. The Velocity decreases as the fluid approaches the stagnation point. The pressure at the stagnation point is the pressure obtained when a flowing fluid is decelerated to zero speed by a frictionless process

## Slide 9
Apply Bernoulli from 1 to 2
 V2
Z
Point 1 = Point 2
P1/air + V12/2g + z1 = P2/air + V22/2g + z2
Knowing the z1 = z2 and that V1= 0, we can simplify the equation
P1/air = P2/air + V22/2g
P1 – P2 = ( V22/2g ) air
 = air

## Slide 10
Bernoulli Assumptions
Key Assumption # 1
Velocity = 0
Imagine a swimming pool with a small 1 cm hole on the floor of the pool. If you apply the Bernoulli equation at the surface, and at the hole, we assume that the volume exiting through the hole is trivial compared to the total volume of the pool, and therefore the Velocity of a water particle at the surface can be assumed to be zero
There are three main variables in the Bernoulli Equation Pressure – Velocity – Elevation
To simplify problems, assumptions are often made to eliminate one or more variables

## Slide 11
Bernoulli Assumptions
Key Assumption # 2
Pressure = 0
Whenever the only pressure acting on a point is the standard atmospheric pressure, then the pressure at that point can be assumed to be zero because every point in the system is subject to that same pressure. Therefore, for any free surface or free jet, pressure at that point can be assumed to be zero.

## Slide 12
Bernoulli Assumptions
Key Assumption # 3
The Continuity Equation
In cases where one or both of the previous assumptions do not apply, then we might need to use the continuity equation to solve the problem
A1V1=A2V2
Which satisfies that inflow and outflow are equal at any section

## Slide 13
Bernoulli Example Problem: Free Jets
What is the Flow Rate at point 2? What is the velocity at point 3?
1
2
3
γH2O
Part 1:
Apply Bernoulli’s eqn between points 1 and 2
P1/H2O + V12/2g + h = P2/H20 + V22/2g + 0
simplifies to
h = V22/2g  solving for V V = √(2gh)
Q = VA or Q = A2√(2gh)
0
A2
Givens and Assumptions: Because the tank is so large, we assume V1 = 0 (Volout <<< Voltank) The tank is open at both ends, thus P1 = P2 = P3 = atm  P1 and P2 and P3= 0

## Slide 14
1
2
3
γH2O
Z = 0
A2
Bernoulli Example Problem: Free Jets
Part 2: Find V3?
Apply Bernoulli’s eq from pt 1 to pt 3
P1/H2O + V12/2g + h = P3/H20 + V32/2g – H
Simplify to  h + H = V32/2g
Solving for V  V3 = √( 2g ( h + H ))

## Slide 15
The Continuity Equation
Why does a hose with a nozzle shoot water further?
Conservation of Mass: In a confined system, all of the mass that enters the system, must also exit the system at the same time.
Flow rate = Q = Area x Velocity
1A1V1(mass inflow rate) = 2A2V2( mass outflow rate)
If the fluid at both points is the same, then the density drops out, and you get the continuity equation: A1V1 =A2V2
Therefore If A2 < A1 then V2 > V1
Thus, water exiting a nozzle has a higher velocity
Q1 = A1V1
A1
V1 ->
Q2 = A2V2
A1V1 = A2V2
A2 V2 ->

## Slide 16
Free Jets
The velocity of a jet of water is clearly related to the depth of water above the hole. The greater the depth, the higher the velocity. Similar behavior can be seen as water flows at a very high velocity from the reservoir behind a large dam .

## Slide 17
The Energy Line and the Hydraulic Grade Line
Looking at the Bernoulli equation again:
P/ + V2/2g + z = constant on a streamline This constant is called the total head (energy), H
Because energy is assumed to be conserved, at any point along the streamline, the total head is always constant
Each term in the Bernoulli equation is a type of head.
P/ = Pressure Head
V2/2g = Velocity Head
Z = elevation head
These three heads summed equals H = total energy
Next we will look at this graphically…

## Slide 18
The Energy Line and the Hydraulic Grade Line
Q
Measures the static pressure
Pitot measures the total head
1
Z
P/
V2/2g
EL
HGL
2
1: Static Pressure Tap
Measures the sum of the elevation head and the pressure Head.
2: Pitot Tube
Measures the Total Head
EL : Energy Line
Total Head along a system
HGL : Hydraulic Grade line
Sum of the elevation and the pressure heads along a system

## Slide 19
The Energy Line and the Hydraulic Grade Line
Q
Z
P/ 
V2/2g
EL
HGL
Understanding the graphical approach of Energy Line and the Hydraulic Grade line is key to understanding what forces are supplying the energy that water holds.
V2/2g
P/
Z
1
2
Point 1:
Majority of energy stored in the water is in the Pressure Head
Point 2:
Majority of energy stored in the water is in the elevation head
If the tube was symmetrical, then the velocity would be constant, and the HGL would be level

## Slide 20
A 7.5 cm diameter hose contains water flowing at the rate of 0.085 m3 /s . If the Pressure within pipe is 70 KPa gauge ,work out the maximum height to which the water may be sprayed ?
26.01m

## Slide 21
A pipe 12.5 cm in diameter is used to transport oil of relative density 0.75 under a pressure of 1 bar .If the total energy relative to datum plane 2.5 m below centre of pipe is 20 Nm/N, Work out the flow rate of oil.
ANS .1074

## Slide 22
The rate of water through a vertical conical draft tube of a kaplon Turbine is 17.5 m3/s.The Diameter of the draft tube on the side connected to outlet of turbine runner is 2.5 m and the average velocity at exit is 1.5 m/s .if pressure at inlet is not to be less than -.7 Bar and at outlet .12 Bar .how far the tube should exrtend above tail race .presume that exit of draft tube is 1.2 m below tail level
Ans 6.595

## Slide 23
A horizontal water pipe of diameter 15 cm converges to 7.5 cm diameter . If the pressures at the two sections are 400 kPa and 150 Kpa calculate the flow rate of water
Notes: <number>
.102 m3/s

## Slide 24
A pipe 12.5 cm in diameter is used to transport oil of relative density 0.75 under a pressure of 1 bar . If total energy relative to datum plane is 2.5 m below the centre of pipe is 20 Nm/N, work out the flow rate of oil.
Notes: <number>

## Slide 25
Modeling and Simulation
Reynolds Number
-Reynolds number is used to characterize the type of flow in a pipe, such as laminar, turbulent
or critical flow
- It is also used to calculate the friction factor in pipe flow
- It depends upon property of gas, pipe diameter etc.
Re = u D d / n
Where
Re- dimensionless, u-average velocity (m/s), D- inside diameter (mm),
d- gas density(kg/m^3), n-gas viscosity (kg /m-s)
Laminar flow – The Re. No. is less than and equal to 2000
Turbulent flow - The Re. No. is greater 4000
Critical flow - The Re. No. is undefined and in between 2000 and 4000
Notes: <number>
<number>

## Slide 26: Laminar and Turbulent Flows
Critical Reynolds number (Recr) for flow in a round pipe
  Re < 2300  laminar
  2300 ≤ Re ≤ 4000  transitional
  Re > 4000  turbulent
Note that these values are approximate.
For a given application, Recr depends upon
  Pipe roughness
  Vibrations
  Upstream fluctuations, disturbances (valves, elbows, etc. that may disturb the flow)
Definition of Reynolds number
Notes: <number>

## Slide 27
Pipe Flow and the Energy Equation
For pipe flow, the Bernoulli equation alone is not sufficient. Friction loss along the pipe, and momentum loss through diameter changes and corners take head (energy) out of a system that theoretically conserves energy. Therefore, to correctly calculate the flow and pressures in pipe systems, the Bernoulli Equation must be modified.
P1/ + V12/2g + z1 =
P2/ + V22/2g + z2 + Hmaj + Hmin
Hmaj
Energy line with no losses
Energy line with major losses
1
2

## Slide 28: Minor Losses
Piping systems include fittings, valves, bends, elbows, tees, inlets, exits, enlargements, and contractions.
These components interrupt the smooth flow of fluid and cause additional losses because of flow separation and mixing
We introduce a relation for the minor losses associated with these components
KL is the loss coefficient.
Is different for each component.
Is assumed to be independent of Re.
Notes: <number>

## Slide 29
Minor Losses
Unlike major losses, minor losses do not occur over the length of the pipe, but only at points of momentum loss. Since Minor losses occur at unique points along a pipe, to find the total minor loss throughout a pipe, sum all of the minor losses along the pipe. Each type of bend, or narrowing has a loss coefficient, KL to go with it.
Minor Losses

## Slide 30
Major Losses
Major losses occur over the entire pipe, as the friction of the fluid over the pipe walls removes energy from the system. Each type of pipe as a friction factor, f, associated with it.
Hmaj = f (L/D)(V2/2g)
Hmaj
Energy line with no losses
Energy line with major losses
1
2

## Slide 31
Major and Minor Losses
Major Losses:
Hmaj = f (L/D)(V2/2g)
f = friction factor L = pipe length D = pipe diameter
V = Velocity g = gravity
Minor Losses:
Hmin = KL(V2/2g)
Kl = sum of loss coefficients V = Velocity g = gravity
When solving problems, the loss terms are added to the system at the second analysis point
P1/ + V12/2g + z1 =
P2/ + V22/2g + z2 + Hmaj + Hmin

## Slide 32: Piping Networks and Pump Selection
Two general types of networks
  Pipes in series
    Volume flow rate is constant
    Head loss is the summation of parts
  Pipes in parallel
    Volume flow rate is the sum of the components
    Pressure loss across all branches is the same
Notes: <number>

## Slide 33
Head Loss due to Sudden Changes in Area of Flow
Sudden Expansion: The head loss at a sudden expansion is given by the expression:
  Sudden Contraction: The head loss at a sudden contraction is given by the expression:

## Slide 34
At a sudden enlargement of water line from 24 cm to 48 cm diameter pipe ,the hydraulic gradient rises by 1cm .calculate the rate of Flow
Notes: <number>
.0327 m^3/s

## Slide 35
A horizontal pipe ,10 cm in diameter , is joined by sudden enlargement to a 15 cm diameter pipe .Water is flowing at the rate of 2 m^3/min.Find the loss of head due to abrupt expansion and pressure difference in two pipes. If change of section is gradual without any loss, what would be change in pressure?
Notes: <number>
0.7 m of water

## Slide 36
Oil of specific gravity 0.8 flows in a 8 cm diameter pipeline . A sudden expansion takes place into second pipeline of such diameter that maximum pressure rise is obtained .if oil flow rate through the pipeline is 12.5 litres / sec find
The loss of energy in sudden expansion in centimeters of oil
The differential gauge length indicated by an oil mercury manometer connected between two pipes
Notes: <number>
1 0.158 m of oil
2 9.875 cm

## Slide 37
Oil of specific gravity 0.8 flows in a 8 cm diameter pipeline . A sudden expansion takes place into second pipeline of such diameter that maximum pressure rise is obtained .if oil flow rate through the pipeline is 12.5 litres / sec find
The loss of energy in sudden expansion in centimeters of oil
The differential gauge length indicated by an oil mercury manometer connected between two pipes
Notes: <number>
1 0.158 m of oil
2 9.875 cm

## Slide 38
A 15 cm diameter pipe is attached to a 10 cm diameter pipe by means of a flange in such a manner that axes of the two are in straight line .Water flows through the arrangement at a rate of 2m^3/min The pressure loss at the transition as indicated by differential gauge length on mercury manometer connected between the two pipes equals 8 cm .calculate the head loss and coefficient of contraction

## Slide 39
A horizontal pipeline 15 am in diameter is joined by sudden enlargement to 25 cm diameter .Measurements indicate that when flow from smaller cross section ,the head loss is 0.5 m in excess of that when flow takes place from larger to smaller section .Determine the flow rate .Take coefficient of contraction Cc =.63

## Slide 40
When a sudden contraction is introduced in a horizontal pipeline from 50 cm diameter to 25 cm diameter,the pressure changes from 105 kPa to 69 KPa .If coefficient of contraction is assumed to be 0.65 , calculate the water flow rate .
The contraction is subsequently followed by a sudden enlargement from 25 cm section to 69 kPa ,work out the pressure at 50 cm enlarged section
Take specific weight of water =10kn/m3

## Slide 42
When a sudden contraction is introduced in a horizontal pipeline from 50 cm diameter to 25 cm diameter, the pressure changes from 105 kPa to 69 KPa .If coefficient of contraction is assumed to be 0.65 , calculate the water flow rate .
The contraction is subsequently followed by a sudden enlargement from 25 cm section to 69 kPa ,work out the pressure at 50 cm enlarged section
Take specific weight of water =10kN/m3

## Slide 43: Pipes series and parallel
Darcy’s equation for head loss due to friction
3
hf = fl(q)
3d^5
hf = head loss
l= pipe length
d= diameter of pipe
f=Co-efficient of friction

## Slide 44
SERIES
Q=Q1=Q2=Q3
hf = hf1+hf2+hf3
PARALLEL
hf = hf1=hf2=hf3
Q=Q1+Q2+Q3

## Slide 45
Two reservoirs are connected by three pipes laid in parallel .The pipe diameters are respectively 10cm,20 cm and 30cm and they are of same length .if discharge through 10 cm pipe is o.1 m^3/s,calculate the discharge through the larger pipes.Assume co-efficient of friction “f” to be same for pipes

## Slide 46
Two pipes each 250 m long are available for connecting to a reservoir from which a flow of 0.08m^3/s is required .The pipe diameters are 10 cm and 20 cm respectively. compare the head loss through the system if the pipe constitute a series and parallel arrangement .Neglect minor losses due to pipe transitions and fittings .Assume f=0.01 .