## Slide 1: ELECTRONICS AND TELECOMMUNICATIONS DEPARTMENT
<number>
A PREPAID WATER CONTROL CIRCUIT SYSTEM FOR WATER METERING
Notes: <number>
Formula for Refractive Index.
A vacuum is the least dense medium, light travels fastest.
Refractive Index of a vacuum is 1.
More dense materials, EG: air, water, and glass, light travels slower.
The refractive Index of air, water & glass is greater than 1

## Slide 2: INTRODUCTION
<number>
A water meter is a device that is used to measure the volume of water usage.
A prepaid water control circuit system is a control mechanism that allows water usage when there is a certain amount of prepaid units in the control circuit system and terminates water usage when the units are over.
In such a system, a customer purchases a separate prepaid credit card with values of credit units encoded in it.
The units are loaded into the control circuit system which allows water usage, when the units are over the control circuit system cuts off water automatically until recharged with new units.
Notes: <number>
In voice and data communications we use two types/construction of fibre, they both have their own pros and cons.
Multimode fibre until recently has been the cable we install for LAN applications.
Due to very high speeds in the backbone, singlemode fibre is now finding a place

## Slide 3: PROBLEM STATEMENT
<number>
The current water metering system is postpaid.
Water authority sends its workers to customer’s locations to read water meter units.
The system is time consuming to the DAWASCO workers.
The system does not give accountability to costumers.

## Slide 4: PROJECT OBJECTIVE
<number>
General objective
The general objective of this project is to design a prepaid water control circuit system for water metering.
Specific objective
To design an electrically controlled valve that will be used to open and close water flow to the customer.
To design sensing system that will generate voltage equivalent to the amount of water used by a customer.

## Slide 5: SIGNIFICANCE OF THE PROJECT
<number>
To reduce or eliminate the expenses of reading meters at the customer’s locations.
To eliminate the bad habit of some customers who load up their bill debts.
To eliminate the expenses incurred by the water authority to cut meters of customers who fail to pay their bills for a long time.

## Slide 6: METHODOLOGY
<number>
Reading different literatures relevant to this project.
Internet surfing for proper materials which will help to accomplish the project.
Consulting the project supervisor, lecturers, qualified professionals, and some water customers.
Data collection
Designing the system.
Testing the system.
Writing the project report.

## Slide 7: LITERATURE REVIEW
<number>
Explains about the literature behind the existing and proposed system.
Also discusses their advantages and disadvantages.

## Slide 8: LITERATYRE REVIEW CONT…
<number>
BLOCK DIAGRAM OF AN EXISTING SYSTEM
REGISTER (READING METER)
WATER OUTLET
WATER INLET

## Slide 9: LITERATURE REVIEW CONT…
<number>
ADVANTAGES OF EXISTING SYSTEM
It is cheap to install.
Requires few components to install.
DISADVANTAGES OF EXISTING SYSTEM
Time consuming to the DAWASCO workers
It does not give accountability to costumers
Some customers complain to be overcharged for small service.
Some customers load up their bills for a long time.

## Slide 10: LITERATURE REVIEW CONT…
<number>
SENSOR
MICROCO
NTROLLER
DISPLAY
VALVE
BLOCK DIAGRAM OF THE PROPOSED SYSTEM
SWITCHING
CIRCUIT
KEYPAD
SOLAR
POWER
SUPPLY
FLOW OF WATER SUPPLY TO A CUSTOMER

## Slide 11: ADVANTAGES OF THE PROPOSED SYSTEM
<number>
The system will eliminate meter reading expenses
The corporation will be able to calculate its income because it will have direct payments for its water supply.
The system will eliminate bad habits of some customers who load up their bill debts.
The system will reduce or eliminate customer’s complains of been overcharged.
The system will provide a great awareness to the customer’s water consumption habits

## Slide 12: DATA COLLECTION EXISTING SYSTEM
<number>
Types of water meter used by DAWASCO | Mult-jet
Max flow rate | 8000 litres/hour
Min. flow rate | 100 litres/hour
Body length | 165mm
Height | 125mm
Width | 100mm
Mass | 475-480gram

## Slide 13: DATA COLLECTION CONT…
<number>
A list of some few customers’ bills complaints.
S/N | Customer name | A/N | Meter No | Area Office Reported | Misreading | Actual reading
1 | Juliana Mtui | A1243501 | 35145518 | Ilala | 520 | 402
2 | Mohamed Habib | 90001910 | 28349182 | Ilala | 195 | 155
3 | Mary Masaro | A126201 | 35114473 | Ilala | 1876 | 1409
4 | Val Nallav Th | 12304201 | 34145450 | Ilala | 674 | 631
5 | Majput C. M | 13104161 | 35106036 | Ilala | 150 | 97

## Slide 14: DATA COLLECTION CONT… PROPOSED SYSTEM
<number>
Technical specification of the tachogenerator sensor
Model 8931 – Speed Sensor / Tachometer | 
Direction of Rotation | CW and ACW
Speed Ranges | 0 to 2500 r/min and 0 to 7500 r/min
Output Voltage | 5V
Input Voltage | 15 V DC
Speed Sensor Output Sensitivity Impedance | 500 r/min / V
 | Less than 15 kΩ

## Slide 15: DATA COLLECTION …
<number>
Technical specification of the tachometer sensor
Model 8920 – Digital Tachometer | 
Direction of Rotation | CW and ACW
Speed Range | 0.05% + 1 digit
Power | four 1.5-V AA cells
Display | 5 digits
Physical Characteristics Dimensions (H xW x D) | 80 x 250 x 120 mm

## Slide 16: DATA COLLECTION …
<number>
General 2x6 Matrix keypad specification
2x6 | Columns and Rows
Contact Rating | 60mA, 5Vdc
Operating temperature | -40°C to +70°C
Storage temperature | -45°C to + 75°C
Operating environment | 100% Relative Humidity

## Slide 17: DATA COLLECTION …
<number>
General 4x4 Matrix keypad specification
4x4 | Columns and Rows
Contact rating | 20mA,24VDC
Contact resistance | 200 ohm max
Operating Temperature | -20°C to +60°C
Storage Temperature | -40°C to +65°C

## Slide 18: DATA COLLECTION CONT…
<number>
General 3x4 Matrix keypad specification
3x4 | Columns and Rows
Contact Rating | 20mA, 5Vdc
Max resistance | 200Ω
Life | 1000000 cycles per day
Operating temperature | -20°C to +60°C
Storage Temperature | -40°C to +65°C

## Slide 19: DATA COLLECTION CONT…
<number>
PIC 16F87X data sheet specifications
Key Features | PIC16F873 | PIC16F874 | PIC16F876 | PIC16F877
Operating Frequency | DC - 20 MHz | DC - 20 MHz | DC - 20 MHz | DC - 20 MHz
FLASH Program Memory (14-bit words) | 4K | 4K | 8K | 8K
EEPROM Data Memory | 128 | 128 | 256 | 256
I/O Ports | Ports A,B,C | Ports A,B,C,D,E | Ports A,B,C | Ports A,B,C,D,E
Interrupts | 13 | 14 | 13 | 14

## Slide 20: DATA COLLECTION CONT…
<number>
Technical specification of the solenoid valve
Size | ¼-1 inches
Material | Brass
Voltage | 5V – 12V
Working Pressure | 6000kPa
Actuator | 90°
Rotational direction | Double Acting
Power | 5W max

## Slide 21: DATA ANALYSIS
<number>
Introduction
This involves selection of the components and either the reasons for the selection of a given particular component or the calculations leading to the selection of the particular component that will eventually be incorporated in building the complete circuit.

## Slide 22: DATA ANALYSIS…
<number>
SENSOR
Tachogenerator sensor will be used. It has:
Speed Ranges of 0 to 2500 r/min and 0 to 7500 r/min
Output Voltage is 5V which does not need to be amplified in order to be compatible with the PIC
Good sensitivity of to 500 r/min / V

## Slide 23: DATA ANALYSIS…
SUPPLIERS PIPE FLOW RATE
Where:-
A = cross sectional area of the inner diameter (m2).
V = water flow velocity (m/sec)
But,
Where:-
r = radius of the pipe(m)
Therefore,
The existing diameter of the pipe = 2½in = 6.5cm

## Slide 24: THE DAWASCO INLET PIPE DATA ANALYSIS
Assuming that DAWASCO will constantly supply water system for 24hours. Thus, the average volume flow rate in DAWASCO inlet pipe,
Therefore the velocity of water in the DAWASCO pipe
is
Where:- Q = volume flow rate (m3/min)
r = radius of a pipe = 0.065m
A = cross section area of a pipe(m2)

## Slide 25: PIPE DATA ANALYSIS…
Therefore velocity,

## Slide 26: DATA ANALYSIS...
<number>
KEYPAD
3x4 matrix keypad will be used in this project.
It is more convenient than 4x4 because it is easy to use, also it is easy to interface with the PIC.

## Slide 27: DATA ANALYSIS ...
<number>
KEYPAD PIN CONNECTION
Wire Color | Description | Pins
Green | Data 0 | Pin 1
- | not used | Pin 2
Red | Keypad Power | Pin 3
Black | Keypad Ground | Pin 4
- | not used | Pin 5
Brown | LCD | Pin 6
White | Data 1 | Pin 7

## Slide 28: DATA ANALYSIS…
<number>
DISPLAY
The display that will be used in this project is a LCD LM020L which has the following parameters
Power supply is +5V
Number of characters is 16character x 1line
Effective display area is (64.5width x 13.8 height)mm
Character size (5x7 dots) is (3.07width x 5.73height)mm

## Slide 29: DATA ANALYSIS…
<number>
MICROCONTROLLER
From the PIC 16F87X data sheet, PIC 16F877 is the best choice since it has a memory large enough to store large data. It has an inbuilt ADC, and it has many I/O ports.

## Slide 30: DATA ANALYSIS…
Relay analysis
The d.c. resistance is 200 ohm ,its related voltage is 12V then the collector current
Selecting transistor BC 108, Si,with Icmax=500mA ,Vcemax=45V
From the data sheet hfe=beta=240
Ptotal=0.5, gain=240 ,Ic=I=88.9ma

## Slide 31: Relay cont….
The Vout is 5V
Vbc = 0.65V
Therefore R is 10k

## Slide 32: RELAY CIRCUIT DIAGRAM BEFORE SIMULATION

## Slide 33: RELAY CIRCUIT SIMULATION RESULTS

## Slide 34: POWER SUPPLY CIRCUIT BEFORE SIMULATION

## Slide 35: POWER SUPPLY CIRCUIT SIMULATION RESULTS

## Slide 36: THE COMPLETE CIRCUIT DIAGRAM BEFORE SIMULATION

## Slide 37: CIRCUIT SIMULATION BEFORE ENTERING NUMBER

## Slide 38: CIRCUIT SIMULATION AFTER ENTERING NUMBER

## Slide 39: CONCLUSION
<number>
The project has successfully taken an initial idea of designing a prepaid water control circuit system for water metering.
The project considered the possibility of having a credit card with loaded data, however, there is a failure in incorporating such credit card in the system and the project ended only at circuit designing.

## Slide 40: RECOMENDATION
<number>
The circuit can be improved in the future design to include the security information such as a unique identical serial control circuit number intended to be used only for a given particular control circuit.
During implementation, the control circuit should be well protected from external damages. It should be installed in a housing and at least one meter from the ground.